## Slide 1: Intro to Signal Processing in Python
Presented by ACM SIGMusic

## Slide 2: What You’ll Need
Python3
  Recommended to install through conda
Numpy
Scipy
Matplotlib
Jupyter-Lab
  The jupyter notebook file that goes with this presentation

## Slide 3: How do computers represent sound?
‘Samples’ of audio taken from the real world at a fixed rate
  This rate is called the ‘sampling rate’ often denoted as fs
  The sample is a bit value corresponding to pressure that the mic picks up at the given time

## Slide 4: More on sampling rate
The sampling rate must be at least twice the frequency of the highest frequency you want to represent on the computer
  Called the Nyquist Frequency
Why? (show image)
Failing to obey this results in aliasing
This is why audio is often sampled at 44.1 kHz or 48 kHz

## Slide 5: Time Domain Representation
Way you generally see audio plotted (like in a recording like audacity)
  The ‘waveform’: x[n] = x[0] + x[1] + x[2] + … + x[n-1]
Great format for some data, but not always for audio
Not really how our brains and ears process audio

## Slide 6: Frequency Domain Representation
Determines weighting of frequencies by viewing the signal as a sum of sinusoids
What’s really important is that this is done with something called a Fast Fourier Transform (FFT)
Periodic about your Nyquist frequency

## Slide 7: What if I don’t care about negative frequencies?
Generally you won’t for audio
Use a real FFT, faster and only positive frequencies

## Slide 8: Time-Frequency Domain Representation
Most of the time audio isn’t a stable frequency all the time, like a sine wave
Solution: take bunch of FFTs in short intervals (windows)
  Short Time Fourier Transform (STFT)
Tradeoff between time and frequency resolution
  Longer window has more accurate frequency distribution, but worse timing accuracy

## Slide 9: Windows
You can take slices of your input signal, but it leads to discontinuities
Solution: Have each window overlap with the next and previous and multiply each by something that smoothes it at beginning and end
  Hanning, Hamming, Kaiser are common

## Slide 10: Filters
Way to manipulate the audio content in interesting ways
  Often used to remove or increase different frequencies in a sound
  Like a graphic equalizer
Two design types
  Finite Impulse Response (FIR) – safe, but more computationally intensive
  Infinite Impulse Response (IIR) – can be unstable, ie. Produce bad output even for safe input

## Slide 11: Filters - 2
Low Pass Filter (LPF)
  Removes high frequencies, lets lows pass
High Pass Filter (HPF)
  Removes low frequencies, lets highs pass
Bandpass Filter (BPF)
  Removes frequencies outside the pass band
Bandstop Filter
  Removes frequencies in the specified band

## Slide 12: How can all of this be used?
Feature extraction
Audio effects
Noise reduction
Preprocessing for machine learning
Data visualization
Beyond music and audio
  I’ve directly applied all of this to medical devices